## Slide 1
The code for data acquisition is composed by two programs, one for Arduino, which takes care of the ADC sampling of two channels and sends the data to the PC via the USB serial port.
The other program, written in Python, reads the data from the USB and stores them in a text file.
The Arduino program samples at a rate of 333kHz and internally saves data using a circular buffer, that has a size of 3332 samples (corresponding to 10 ms).
After the trigger is enabled, 2667 samples (corresponding to 8ms) are recorded and the whole buffer (containing also 2 ms captured before the trigger) is sent to to the USB serial port (lasting 4.4 ms).
See:
Arduino due processor datasheet:
https://ww1.microchip.com/downloads/en/DeviceDoc/Atmel-11057-32-bit-Cortex-M3-Microcontroller-SAM3X-SAM3A_Datasheet.pdf
Arduino due unofficial pinout:
http://www.robgray.com/temp/Due-pinout.pdf */
# define BUFFER_SIZE 3332
# define POST_TRIGGER_SAMPLES_NUM 2667

## Slide 2
The circular buffer and the samples are defined through appropriate data types.
A single acquisition is organized in a data type called Sample, that contains the 2 ADC readings I and Q and the corresponding reading time in micros.
The circular buffer has two attributes:
buffer: a pointer to an array of samples
end : the index of the next position of the buffer to be filled
typedef struct {
int I, Q; // 4 bytes each
unsigned int t; // 4 bytes
} Sample; // 12 bytes
typedef struct {
Sample *buffer;
int end;
} CircBuffer;
// method to set up the circular buffer
void circ_buffer_setup(CircBuffer *c, Sample *b) {
c->end = 0;
c->buffer = b; // inizializes the buffer to an array
}

## Slide 3
The setup continues with USB serial port initialization; note that SerialUSB refers to the Arduino Native USB Port, which is faster than the Programming Port.
Then we allocate memory, set up the circular buffer and initialize to zero the last element of the buffer, that will be used to report the amount of time needed to send the data (this information is useful to control dead time).
void setup() {
SerialUSB.begin(115200); // initializes the serial port and sets the baud rate
// wait for python to open the serial port
while (!SerialUSB);
circ_buffer = (CircBuffer*) malloc(sizeof(CircBuffer));
buffer = (Sample*) malloc(sizeof(Sample)*(BUFFER_SIZE + 1));
circ_buffer_setup(circ_buffer, buffer);
buffer[BUFFER_SIZE] = {0, 0, 0};
...
}

## Slide 4
In order to maximize the sampling rate, in the Arduino setup method we explicitly set the ADC registers.
Usually, the ADC only perform conversions when started with a hardware or software trigger (like in the case of analogRead).
On the contrary, here we set up:
Free Running Mode: the ADC does not wait for any trigger or instruction to start conversion
Fast Wake Up Sleep Mode: between two conversions the Voltage reference is ON and the ADC Core is OFF
Then the ADC reading is enabled only for A0 and A11 pins. The reason for choosing the most distant ones is to avoid possible cross-talks.
void setup() {
...
// sets free running mode (7th bit) and fast wake up (6th bit)
// see page 1333 of the datasheet
ADC->ADC_MR |= 1 << 7 | 1 << 6;
/* see the pinout for the mapping between Arduino pins and ADC channels
* ch7: A0, ..., ch0: A7 - ch10: A8, ..., ch13: A11
*/
I_CHANNEL_NUM = 7; //A0
Q_CHANNEL_NUM = 13; //A11
// see page 1338 of the datasheet
ADC_CHANNELS = (1 << I_CHANNEL_NUM) | (1 << Q_CHANNEL_NUM);
ADC->ADC_CHER = ADC_CHANNELS; // enables channels
ADC->ADC_CR |= 1 << 1; // begins ADC conversion (1st bit on)
...
}

## Slide 5
// Method that acquires data, puts them in the buffer as a Sample and returns the pointer to it
Sample * acquire_data() {
// after declaring p, assigns to it the pointer to the Sample that will be filled
Sample *p = &(circ_buffer->buffer[circ_buffer->end]);
// puts ahead the buffer index
circ_buffer->end = (circ_buffer->end + 1) % BUFFER_SIZE;
// waits until ADC conversion is completed for both channels
while((ADC->ADC_ISR & ADC_CHANNELS)!=ADC_CHANNELS);
p->I = ADC->ADC_CDR[I_CHANNEL_NUM]; // read value of I
p->Q = ADC->ADC_CDR[Q_CHANNEL_NUM]; // read value of Q
p->t = (unsigned int)(micros() - start_micros);
return p;
}
// Method to send one bunch of data to python
void send_data() {
start_sending_micros = micros();
// in order to reduce dead time, data are sent to python all in one time as an array of bytes
SerialUSB.write((byte*)buffer, sizeof(Sample)*(BUFFER_SIZE + 1));
// saves the time needed by arduino to send data
buffer[BUFFER_SIZE].Q = micros() - start_sending_micros;
}
Here we define the methods used to acquire from ADC and to send data to python.

## Slide 6
The trigger method is just a simple condition on the I channel read int value, which in this case corresponds to 20*Vref/(4096-1) Volts, where standard Vref=3.3 Volts for Arduino Due.
In the future the condition for triggering will be developed as a combination of I and Q channel (maybe I^2+Q^2)
int trigger(Sample *s) {
if (s->I > 20){ // just a reasonable number for now
return 1;
}
else return 0;
}

## Slide 7
The loop function is designed such that Arduino only reads when Python is
ready to save data and exactly for the amount of time dictated by Python.
This purpose is achieved by using an handshake.
void loop() {
// polls whether anything is ready on the read buffer
// nothing happens until python writes the acquisition time (in s) to the serial
if (SerialUSB.available() > 0) {
// handshake - start ----------------------------
//waiting a little time for arduino to be ready to receive data
delay(100); // ms
// reads from python the acquisition time in seconds
acquisition_time_millis = SerialUSB.readString().toInt()*1000;
// after receiving the value, sends back it in milliseconds to complete handshake
SerialUSB.println(acquisition_time_millis);
//waiting a little time for python to be ready to receive data
delay(100); // ms
...
}

## Slide 8
The acquisition is performed with a simple while loop, however, when the trigger gets activated,
exactly POST_TRIGGER_SAMPLES_NUM samples (8 ms) of data are recorded with a for loop.
At the end of the for loop, the buffer (containing 10 ms of data) is sent over the serial port.
void loop() {
...
end_millis = millis() + acquisition_time_millis;
start_micros = micros();
while (millis() < end_millis) {
s = acquire_data();
if (trigger(s)) {
for(i=0; i<POST_TRIGGER_SAMPLES_NUM; i++) {
acquire_data();
}
send_data();
}
...
}